## Slide 1
Predictive Maintenance: the Decision Engine
• Project #3 — the layer between prediction and action
• Mukesh Sharma · github.com/designmukesh
• Builds on: hydraulic fault classification (#1) + turbofan RUL (#2)

## Slide 2
The gap this closes
• Models answer 'what is the condition?' — planners need 'what do we do Tuesday?'
• Most pilots die at the handoff: accurate model, no decision policy
• This project engineers the handoff: costs → rule → backtested policy

## Slide 3
Cost model (assumed, labeled)
• planned intervention = 1.0 (numeraire)
• unplanned failure = k × planned, k ∈ {3, 5, 10} scenarios
• inspection = 0.1 · lead time = 1 cycle
• Only the ratio k matters for the decision

## Slide 4
The decision rule
• Act when E[cost of waiting] > E[cost of acting]
• p(fail) × C_u > C_p ⟺ p > 1/k
• p from 3,524 OBSERVED residuals — no assumed Gaussian
• Thresholds from economics, not folklore

## Slide 5
Backtest design
• 20 validation engines, out-of-sample RUL predictions
• Full run-to-failure trajectories — true failure known, bills exact
• Three policies: run-to-failure · fixed-interval (N) · predictive (T)
• Sweep T 0–60; sensitivity over k = 3 / 5 / 10

## Slide 6
Results (k=5, illustrative)
• Run-to-failure: 5.0/engine, 20/20 unplanned failures
• Fixed-interval N=25: 1.0/engine
• Predictive T*=8: 1.0/engine, 0 unplanned, least wasted life
• Ranking holds across all k scenarios

## Slide 7
Two honest surprises
• Cost curve is L-shaped, not U-shaped — wasted life isn't monetized
• T* doesn't move with k here: k prices timidity, not the optimum
• Selection is lexicographic: min cost, then min wasted life
• Flat bottom = threshold error is cheap (good for deployment)

## Slide 8
Hydraulic fault policy
• Auditable table: (component, fault state) → operate/monitor/inspect/replace
• 1,764 held-out predictions: expected action cost 0.295/cycle
• 1 missed severe state in 380 — the residual risk, stated plainly

## Slide 9
Deploying it
• Policy service: predict → decide → work order
• Re-estimate the residual distribution as field data arrives
• Monitor two vital signs: slip rate + wasted healthy life
• Next step: field pilot with holdout fleet — not a rollout

## Slide 10
Takeaway
• The method is the deliverable — any planner's costs plug in
• 14 tests · 2 executed notebooks · interactive Streamlit app
• Limitations volunteered: assumed costs, n=20, single failure mode
• Questions?